## Slide 1: Account and Resource Management 1 File and Printer Sharing
IT&C 344 – S04

## Slide 2: In the days before the internet…
We had local-area networks (LANs)
What was a LAN used for?
Image: DALL-E

## Slide 3: What was a LAN used for?
File Sharing
Printer Sharing

## Slide 4
Networking in the ‘90s
7. Application
4. Transport
3. Network
2. Data Link
1. Physical
6. Presentation
5. Session
Ethernet
Token Ring
ArcNet
IP
IPX (Novell)
TCP, UDP
SPX (Novell)
NetBEUI (Microsoft)
NFS LPR
NCP (Novell)
SMB (Microsoft)
LocalTalk (Apple)
COAX
Fiber
CAT-3
CAT-5
Radio
HTTP, FTP, SSH, etc.
Notes: Ethernet and Token Ring were competing for best performance. Ethernet ultimately won with the introduction of 100-Base-T and, especially, switching.
Localtalk was Apple’s proprietary network and only worked on Macintosh computers. It was abysmally slow at only 256Kbps.
IP is routable and forms the basis of the internet
IPX was technically routable, but no-one built routers for IPX and that contributed to its downfall.
However, IP requires each device to be configured with an IP address, network address, and subnet mask. SPX, NetBEUI, and LocalTalk self-configure so it took longer for IP to catch on in home and small-business use.
Ultimately, the combination of DHCP (for auto configuration) and the pull of the internet caused IP to win.
Technically these protocol stacks can co-exist. I had a windows XP machine running IP, IPX, and NetBEUI all at the same time.

## Slide 5
Networking in 2005 through Today
7. Application
4. Transport
3. Network
2. Data Link
1. Physical
6. Presentation
5. Session
Ethernet
Token Ring
ArcNet
IP
IPX (Novell)
TCP, UDP
SPX (Novell)
NetBEUI (Microsoft)
NCP (Novell)
SMB (Microsoft)
LocalTalk (Apple)
COAX
Fiber
CAT-3
CAT-5
Radio
NFS IPP
HTTP, FTP, SSH, etc.
WiFi

## Slide 6: Printer and File Sharing Protocols
Linux
Windows
NFS: Network File System
IPP: Internet Printing Protocol
SMB: Server Message Block
Samba
Client for NFS (optional feature)
LPR/LPD: Line Printer Remote (legacy)
IPP Client (since Windows 10)
LPR Port Monitor (optional feature)

## Slide 7: What about macOS?
NFS: Network File System
IPP: Internet Printing Protocol
SMB: Server Message Block
LPR/LPD: Line Printer Remote (legacy)
macOS
Notes: In a surprise departure from Apple’s typical walled garden, macOS supports all of the above.

## Slide 8: How do you share and backup files in 2024?
Sync (plus online)
Sync (plus online)
Online (manually drag-drop)
Online
Sync or Online
One at a time
One at a time
One at a time
None of these are real-time file sharing like NFS and SMB support!
iCloud
OneDrive
Google Drive
Box.com
Dropbox.com
Email
Slack
Discord
Notes: These all use the web and web protocols.
If someone mentions NAS – that DOES use file sharing protocols. Most NAS boxes support both NFS and SMB.

## Slide 9: How do you print in 2024?
Printer Discovery Protocols
Bonjour – device discovery for Macs
  Available as an add-in for Windows
LLTD –device discovery for Windows
  Link Layer Topology Discovery
  Operates at Layer 2 – not routable
SNMP – Simple Network Management Protocol
SMB – Server Message Block
  Includes device discovery among its capabilities
UPNP – Universal Plug and Play
  Supports device discovery
  Mostly associated with router discovery and automated port forwarding (which can be a security issue).
  Equally effective for discovering printers and not a security issue in that context.
WINS – Windows Internet Name Service
  A routable protocol for name discovery and name to address translation.
Printer Communication Protocols
SMB – Microsoft file and printer sharing
LPR – Line Printer Remote (legacy but still used a lot)
IPP – Internet Printing Protocol (new and growing in use)
RAW – Raw sending directly to the printer

## Slide 10: Security Issues – File Sharing
Confidentiality
Who can access shared files?
What administrative permissions do they have?
Availability
RAID redundancy (more about this in the Storage Devices unit)
Power Supply
Redundant Network
Integrity
What access do users have (create, read, write, delete)?
Backups
How to detect and correct problems?

## Slide 11: Security Issues – Printer Sharing
Confidentiality
Where is the printer physically located?
Availability
Who replaces printer supplies (paper, toner)?
Integrity
Who can use the printer?
Who bears the cost of printing?