## Slide 1: Devices, I/O, and Device Drivers
IT&C 344 – S21

## Slide 2: In the olden days…
Read/Write
Memory / Port
Clock
Address Bus (16 bits = 64KB)
Data Bus (8 bits = 1 Byte at a time)
CPU
Regular read and write instructions access memory space. E.g. MOV instructions.
IN and OUT instructions access ports.

## Slide 3: Memory-Mapped I/O
Physical Memory Space
0
0xFFFF
Random Access Memory (RAM)
Empty Space
Memory-Mapped I/O
Devices can be mapped into memory space instead of I/O space and so regular MOV instructions can be used to access them.

## Slide 4: A Contemporary CPU…
CPU
PCIe Channels appear in the memory space of the CPU.
Writing to certain memory addresses results in messages sent to the corresponding PCIe Channels
IN and OUT instructions are obsolete. But compatibility hardware still supports them.
Memory Controller
RAM DIMMS
PCIe Channels
Devices
I/O Controller

## Slide 5: Direct Memory Access (DMA)
CPU
The CPU can command a device to read or write directly to memory.
CPU commands device to begin data transfer (e.g. drive to memory).
Device performs the data transfer.
Device interrupts the processor indicating that transfer is complete.
This is much faster than having the CPU read data from a device and write it to memory.
Memory Controller
RAM DIMMS
PCIe Channels
Devices
I/O Controller

## Slide 6: Processor Interrupt
CPU
Devices can interrupt the CPU when they need service:
Data ready from storage
A network packet arrived
A key pressed on the keyboard
A mouse moved
A timer interval expired
The processor saves the state of the current thread, switches to kernel mode, and services the interrupt.
Software can also generate “software interrupts” using the INT or SYSCALL instructions. These are used to make calls from user mode into the operating system.

## Slide 7: PCIe is a High-Speed Network
PCIe Root Complex
Root Port
Root Port
Root Port
Root Port
Root Port
GPU
SSD
Network Adapter
PCI-PCI Bridge
Audio
PCI-USB Bridge
(It’s not a bus.)

## Slide 8: Serial vs. Parallel
Clock
8 Bits
Parallel transmits 8 bits (or more) at a time. So, it should be 8 times faster, right?
start bit – data bits – stop bit
Serial sends one bit at a time.
When speeds are in the gigabits per second it’s hard to synchronize the bits in a parallel connection. A bend in the traces on a circuit board will get them out of sync.

## Slide 9
Serial
Parallel
Peripheral Component Interconnect (PCI)
Advanced Technology Attachment (ATA)
Computer I/O
Storage Drives
Serial ATA (SATA)
PCI Express (PCIe)
Parallel Port
Printers
Universal Serial Bus (USB)
Serial connections have repeatedly replaced parallel as speeds have increased.
A PCIe device such as a GPU can have 16 “lanes” or evem more. But each lane transmits separately. Thre is no synchronization across lanes. So, it’s not a parallel connection.

## Slide 10: Device Drivers
Each device must have a device driver.
A device driver is software that knows how to communicate between the device and the operating system.
The operating system reads a unique identifier from the device and uses that to find the appropriate driver.

## Slide 11: Driver Security
A device driver must run within the kernel in order to have the privileges needed to communicate with the I/O channels.
A security vulnerability in a device driver is more serious than one in an application because the code is running with Kernel privileges.